## Slide 1: An Emulation Framework for Electric Vehicle Charging Using IEC-61499 Function Blocks
Project 72
Supervisor: Dr Partha Roop
Researchers: Sanath Vettivel & Heimana Palmer

## Slide 2: Background
Electric vehicles are becoming more popular.
Electric vehicles need to be charged.
How can we minimise the cost of charging them?
https://www.autoevolution.com/news/america-s-first-high-power-ev-charging-station-has-begun-its-construction-phase-114012.html

## Slide 3: Representation of EV Charging Station

## Slide 4: Related Work

## Slide 5: Related Work
Time of Utilization Pricing Management to minimise the cost of charging
  Current research uses algorithmic approach -> Bollinger Bands
Problem of uncoordinated electric vehicle charging demand due to less involvement of customers
  Solved with Energy Storage System
Energy storage system key in minimising undesired effects of the load on grid
  Large number of uncoordinated demand could have unfavourable effects on grid performance and efficiency

## Slide 6: Related Work
Research model end-users demands to be exactly met by energy supply of the grid
Recognise that compromising charging time to minimise cost is not an option
Installation / running costs of energy storage system unit
  Economic Analysis needed

## Slide 7: MATLAB Algorithm
Repeat process for each day
Print Data
Load EV Data
Generate EV
Energy Demand Per Minute
Decide ESS Mode of Operation
Sum Energy Demand For Each Minute

## Slide 8: Research Intent
We wanted to minimise the cost electric vehicle charging.
We are going to achieve this using an accurate simulation environment built with industry standard IEC-61499 function blocks.
Different research algorithms will be used to try minimise the cost.
Notes: An accurate simulation environment built with industry standard IEC-61499 Function Blocks what we can use to research different algorithms for minimising the cost of EV charging.

## Slide 9: Methodology

## Slide 10: Methodology Overview
Model the Power Demand of Electric Vehicle Users
Energy storage system modes of operation
Implement MATLAB Algorithm into Industry Standard IEC-61499 Function Block Environment
‘Swap-in’ other Researched Algorithms to test which minimises charging cost

## Slide 11: i. Modelling the Energy Demand - Example
Assumption: SoC of all cars are under 80%.
Ereq = 38.77 + 35.89 + 39.1 +5.44 + 6.3 + 5.1 + 5.1 = 135.7 kWh
5 Fast Charging Ports
15 Normal Charging Ports
BMW i3
Nissan leaf
Kia Soul
38.77 kWh
35.89 kWh
39.1 kWh
5.44 kWh
6.3 kWh
5.1 kWh
5.1 kWh
Note: Project models a Public Singaporean Charging Station with 5 Fast Charging Ports (Higher Voltage) and 15 Normal Charging Ports

## Slide 12: ii. Energy storage system - Modes of Operation
On-peak
Off-peak charging
Off-peak
High Demand
High Demand
Low Demand &&(high or medium price)
Low Demand &&(high or medium price)
Low Demand && low price
Low Demand && low price

## Slide 13: ii. Energy storage system – Modes of Operation
On-peak | Off-peak | Off-peak Charging
Priorities use of energy storage system. Grid can supply if need be. | Priorities use of Grid (For Set Amount). Energy storage system can supply rest if need be. | The Grid charges both electric vehicles and the energy storage system.

## Slide 14: iii. Industry Standard IEC-61499 Function Blocks
Provides coordination between multiple programmable logic controllers.
  Object-Oriented Programming
  Function Blocks (FBs)
Advantages:
  Compatible with Multiple Devices (e.g. Microcontrollers, PLC and Sensor)
  Could Interpret the data from multiple software tools
  Interoperable and Event-Driven Execution

## Slide 15: IEC-61499 Basic Function Block (BFB) Interface
https://www.controldesign.com/articles/2007/202/

## Slide 16: Basic Function BLOCK SIMPLE Example
printf( " Hello World " );

## Slide 17: IEC-61499 Composite Function Block (CFB)
https://www.holobloc.com/papers/iec61499/overview.htm
Event Input
Data Input
Event Output
Data Output

## Slide 18: Project Working Environment

## Slide 19: Simplified Overview of Function Block Environment
Input Load Power Demand and Price
ESS Controller
ESS State of Charge Calculations
Grid Energy Calculation
Print Results

## Slide 20: Algorithms (i) Bollinger Bands (ii) Box and Whisker (iIi) Artificial Neural Network

## Slide 21: Algorithm One : Bollinger Bands

## Slide 22: Algorithm two : Box and Whisker
Input Load Power Demand and Price
ESS Controller
ESS State of Charge Calculations
Grid Energy Calculation
Print Results

## Slide 23: Algorithm three : Artificial Neural Network
Predicts likely mode of operation from five inputs
Neural Network has three layers
Trained using Reinforcement Learning
Works for data (electricity price and energy demand) it was not trained for too
Input Load Power Demand and Price
ESS Controller
ESS State of Charge Calculations
Grid Energy Calculation
Print Results

## Slide 24: Results

## Slide 25: Comparison of Algorithms

## Slide 26: Comparison of Algorithms

## Slide 27: Conclusions
Built a simulation environment with industry standard IEC-61499 Function Blocks
  Research different algorithms for minimising the cost of electric vehicle charging.
Testing of algorithms proved the Artificial Neural Network to be best for real time.
Future work could involve our system being able to load Electricity price from online.
Future work to estimate the ‘break-even’ time after initial capital costs for installation.
Improve on each individual algorithm.

## Slide 28: Acknowledgements
Dr Partha Roop
Dr Abhisek Ukil
Mr Hammond Pearce
Mr Kalpesh Chaudhari
Mr Keyan Monadjem

## Slide 29: Appendix

## Slide 30: Modelling the Energy Demand
5 Fast Charging station
15 Normal Charging Station

## Slide 31: Modelling the Energy Demand
Dk: Distance car has travelled (Random Normal Distribution)
Dmax: Maximum distance the type of car can travel
SOCi : Initial State of Charge of Car Battery
SOCf : Initial State of Charge of Car Battery (Random Normal Distribution)
SOCb : State of Charge of Energy Storage System at any minute
Pbc : Charging Power of the Energy Storage System
Pbd : Discharging Power of the Energy Storage System
P1Cb :Power Required by Energy Storage System to charge 100% in 1 hour (i.e. 1C rate)

## Slide 32: Bollinger Bands
Bollinger Bands approach based on related works
Uses Wholesale Electricity Price:
  Simple Moving Average
  Upper Band -> Based on Half of Standard Deviation
  Lower Band -> Based on Half of Standard Deviation
R(k): Electricity Price
n : Number of steps used in Simple Moving Average
SMA : Simple Moving Average

## Slide 33: Calculating the Cost

## Slide 34: Artificial Neural Network
Inputs:
  Wholesale Electricity Price (Present minute and Future minute)
  Energy Demanded by electric vehicles at charging station (Present minute and Previous minute
  State of Charge of Energy Storage System (SoC)
Predicts likely mode of operation:
  On-Peak, Off-Peak, Off-Peak Charging
Neural Network has three layers
Trained using Reinforcement Learning
Works for data (electricity price and energy demand) it was not trained for too

## Slide 35: Disadvantage of Bollinger bands
https://www.researchgate.net/figure/Wholesale-Electricity-price-for-a-typical-day-and-price-band-allocation_fig2_308804006

## Slide 36: Advantages of IEC-61499
Reusability
Component reuse
Portable
Ability of a system to run under different computing environments (moved from one system to another)
Interoperable:
Ability of two or more systems to cooperate at runtime.
Event-triggered:
In event-triggered control, all communication and processing activities, are initiated whenever a significant event other than the regular event of a clock tick occurs.

## Slide 37: ESS Details
Capacity: 620 kWh
Discharge: 200 kWh
Charge: 150 kWh
Why was this chosen?
  Battery capacity for four hours (150 kWh for 4 hours) .
  150 kW chosen due to handle peaks (related work).